## Slide 1: TOWARDS ZERO-WASTE STRUCTURES THROUGH INTEGRATION OF RECLAIMED WOOD AND 3D PRINTING
P5 Presentation
Aron Arend Bakker
5658004

## Slide 2: Context
40% of primary energy goes to the building industry (European Commission, 2017)
The EU pushes for greater reuse of building components (Didier, 2018)
Chart: 
| Other | Building industry
Primary energy demand | 60 | 40

## Slide 3: Circularity
https://www.google.nl/url?sa=i&url=https%3A%2F%2Fwww.forfreechoice.org%2Ffreedomofchoice%2Fcircular-economy%2F&psig=AOvVaw3vGkHZZTIwZ37z1rRQAiNr&ust=1719046886970000&source=images&cd=vfe&opi=89978449&ved=0CBEQjRxqFwoTCJC2oPKq7IYDFQAAAAAdAAAAABAR

## Slide 4: What is the circular economy?
https://www.inboundlogistics.com/articles/the-road-to-the-circular-economy/

## Slide 5: Current standing….
Chart: 
| Biomass | Recycling | Transported | Reuse
End of life wood | 63 | 24 | 21 | 0.5
https://www.mrw.co.uk/subject/editorial/page/1063/?cmd=pagesize&val=20

## Slide 6: So, what seems to be the problem?
Circular material hubs provide storage
A dynamic stock of elements increases complexity
Stock constrained design tools give complex connections
Connections damage the reused elements.
Remanufacturing is required, creating saw-off losses.
Design with a constrained stock increases the complexity of a design project
https://www.freepik.com/premium-photo/process-manual-sawing-timber-man-sawing-timber-when-building-house_27069459.htm

## Slide 7: For example:
Like IKEA without instructions
None of the right elements
Nothing matches
https://www.shutterstock.com/nl/image-photo/worried-woman-moving-into-new-apartment-663880423
https://vimeo.com/654116098

## Slide 8: How can we solve this problem?
Stock-constrained design
Example: Reused/New elements
Example of stock-constrained designed structure
https://www.epfl.ch/labs/sxl/tools/phoenix3d/

## Slide 9: What is stock constrained design?
https://www.epfl.ch/labs/sxl/tools/phoenix3d/

## Slide 10: Disadvantages stock-constrained design
Creates complex and unique joints
Will use larger elements than necessary, creating saw-off loss
Fills gaps with new elements
https://www.researchgate.net/figure/a-shows-the-optimal-structure-designs-and-element-usage-for-stocks-A-B-and-C-when_fig3_354270307

## Slide 11: The proposed solution!
Make connections grow towards elements
Element >= element required
No saw-off!
Substract material
Add material
https://external-content.duckduckgo.com/iu/?u=https%3A%2F%2Fi.redd.it%2Fnssgg09wcxe31.jpg&f=1&nofb=1&ipt=14d75fbdc56d6c583a62013f21d4a5b4d418125f0cd4cbf65037c5e64c2f6f06&ipo=images

## Slide 12: How? Topology optimization + 3D printing
https://www.researchgate.net/figure/3D-printed-wooden-furniture-connectors-2_fig1_375886252

## Slide 13: The research question
“Can stock-constrained digital design combined with 3D printing support the reuse of wooden structural elements without saw-off losses in a sustainable way?”

## Slide 14: The desired end results
A design tool
LCA results
Chart: 
| Scenario 1 | Scenario 2 | Scenario 3 | Scenario 4 | Scenario 5
Carbon footprint | 7 | 6 | 3 | 2 | 1
?
?
?
?
?

## Slide 15: The casestudy

## Slide 16: The scenario’s

## Slide 17: Scenario 1

## Slide 18: Scenario 2

## Slide 19: Scenario 3

## Slide 20: Scenario 4

## Slide 21: Scenario 5

## Slide 22: The scenario’s
Scenario 1
Scenario 2
Scenario 3
Scenario 5
Scenario 4
Chart: 
| Scenario 1 | Scenario 2 | Scenario 3 | Scenario 4 | Scenario 5
Carbon footprint | 7 | 6 | 3 | 2 | 1
?
?
?
?
?

## Slide 23: The workflow
The stock
Creation of the raised roof frame
Creating the freedom of motion
Stock-constrained optimization
Setup for geneation of the joints
Generating
LCA results

## Slide 24: The stock
Reclaimed timber
Circulair hub
3D-digital copies for library
https://encrypted-tbn2.gstatic.com/images?q=tbn:ANd9GcSnmCTwDgEoYhbhAsd5nQcgTsUhzaNseO4IdkPnF7eGr_m657ch

## Slide 25: Recreating the original structure
Original
New wood
Reused wood

## Slide 26: Creating freedom of motion
Optimized design
Optimized connections

## Slide 27: Reuse optimizations
Element >= element required
No stock-constrained optimization
With saw-off losses
Element >= element required
With stock-constrained optimization
With saw-off losses
Element <= element required
with stock-constrained optimization
Without saw-off losses
Reused wood
Optimized design
Optimized connections

## Slide 28: Creating the printable box
What goes into the connection?
Angles, profiles, position etc.

## Slide 29: Loads and materials

## Slide 30: Loads and materials
Material properties:
Density
Youngs modulus
Poisson ratio
https://encrypted-tbn1.gstatic.com/images?q=tbn:ANd9GcSzZsLJse_5FgLFHTOW3mvdlX8zKNwt1QMERN81_ArgzWGVJR25

## Slide 31: Predefined settings

## Slide 32: Generating the connections

## Slide 33: The first result
Fast calculation time
Low resolution
65.176 cm3

## Slide 34: Higher resolution
Slow calculation time
High resolution
-54% volume
29.781 cm3

## Slide 35: Higher iso-value
Takes away “underutilized material”
-67% volume
21.438 cm3

## Slide 36: Smoothening surface
Turning pixels into an surface
-74% volume
16.673 cm3
Old surface
New surface
>

## Slide 37: The waste and LCA results
https://encrypted-tbn3.gstatic.com/images?q=tbn:ANd9GcSsi6Gw9_bk6TpXALxDeBsw3UhJFag9pE-05q5rSRBoMADt6-Uj

## Slide 38: Waste production results
Chart: Waste production of the structure
| 1st service life | 2nd service life | 3th service life | 4th service life
Original | 0 | 1238.1 | 2476.2 | 3714.3
New wood | 0 | 472.4 | 944.8 | 1417.2
Reused wood | 70.8 | 141.6 | 212.4 | 283.2
Optimized structure | 0.85 | 1.7 | 5.1 | 20.4
Optimized connection | 0 | 0 | 0 | 0

## Slide 39: The LCA results
Chart: Carbon footprint comparison 1, 5 and 10 years
| Total Water (L)
Scenario 1 | 1190
Scenario 2 | 267
Scenario 3 | 160
Scenario 4 | 134
Scenario 5 | 1129

## Slide 40: What happend?
https://encrypted-tbn3.gstatic.com/images?q=tbn:ANd9GcS7o5DeFLZlv9P7JNIvlaAqAvFkXtTIzXt0KLjjl1q4HJXLrKv_

## Slide 41: How is this possible?
177 kg plastic
49 kg steel connections
Volume increase 25x
PETG
Steel

## Slide 42: Conclusion
The question
“Can stock-constrained digital design combined with 3D printing support the reuse of wooden structural elements without saw-off losses in a sustainable way?”
My answer
Yes, it is possible to use this method and design with zero waste
However, it might not always be the most sustainable option when compared to the alternatives

## Slide 43: Discussion
Structural validation of the connections
Topos is limited for detailed work

## Slide 44: Discussion
A working attachment that survives the simulation
Attachment could be optimized to save material

## Slide 45: Discussion
Scale was limited during the research

## Slide 46: Discussion
Fire safety
Unthreaded wood + plastic connections
https://vimeo.com/654116098
https://encrypted-tbn0.gstatic.com/images?q=tbn:ANd9GcReQOmKLDCkklg_0-Htpmqauy8e6xQc0IsyrMUvzLUXlhAgjHSf

## Slide 47: Oportunities
Different materials could lead to a more sustainable product
https://encrypted-tbn1.gstatic.com/images?q=tbn:ANd9GcSzZsLJse_5FgLFHTOW3mvdlX8zKNwt1QMERN81_ArgzWGVJR25

## Slide 48: Oportunities
More materials become available to designers with the help of the developed tool
The supplies can come from more local places
https://encrypted-tbn0.gstatic.com/images?q=tbn:ANd9GcTZwYWrrfb0sGKMYt0QLIg65a1mBSvS33t8uacb3xyIMek6b4Sy

## Slide 49: Oportunities
Only energy goes into the created stream
If the energy is CO2 neutral, so is the product
https://encrypted-tbn3.gstatic.com/images?q=tbn:ANd9GcQt2tP1CjfXCJEtVc9YcuILBk0FTOljrHCGuvfJaijU0Fzj5wXi

## Slide 50: Reflection
Easy to compare strategies in a early design stage
Results might change in the future with new materials and different energy sources

## Slide 51: Thank you